## Slide 1: A Franco-German Project for the Online Security Management of Water Distribution Networks Funded by the German Federal Ministry of Education and Research and the French Agence National de la recherche (ANR)
18. March 2015 - Dresden

## Slide 2
Why is this project of importance
What are the goals and the results
How to move forward…
Notes: First I´d like to talk about… and the motivation for doing this research work from the End Users perspective
secondly what are the …
And finaly what are the next step to implement the results

## Slide 3: Ensuring the security of the water supply – one of the major challenges of the 21st Century
Berlin
ca. 900 km²
Paris
(Urban)
ca.700 km²
London
1,579 km²
Strasbourg
ca. 80 km²
Notes: This silde should demonstrate that in all the european cities, no matter how big they are, a SAFE water supply is not an issue any more.
Every one in his Water company works hard and succeed to supply the citizens with satifaing quality and quanittiy of water.
But the simultaneously and constantly monitoring of these larg pipe networks is simply not possible yet

## Slide 4
Urban area: 900 km²
Population: ~ 3.5 Million
Population density: 3,800 inhabitants /km²
Green areas: 35 %, water surface 7 %,
An Example: Berlin
daily demand: ~ 530,000 m³
7,900 km pipe network,
273,000 house connection
groundwater only
No chlorine
No Reservoirs, No towers
Notes: Message: An accident (contamination) has a huge impact,
So we need sensors to monitor in real time

## Slide 5
Current Situation
Aquabiotox:
a broad band (4) sensors in one for online detection of contamination in the water
KAPTA™3000-AC4 water quality parameters
Bio-monitors using Daphnia or fish
quality parameters and TOC
Sensors alone are not the solution!
Notes: As you surly know, during the last decade there have been many projects dealing with developing sensors to detect contamination. One was Aquabiotox; a broad band sensor for continuous detection of hazardous contamination in the water network in a very short period of time. Many other have also been during this time, and many others will be developed in the future, as this is an on going procedure.

## Slide 6
What we need is …
A decision support tool to initiate the right action for each situation
which sensors and where to place them
what to do in case of an alarm
Notes: Let´s say we already have different types of sensors; The First question will be then where to place them and what action should be taken when a sensor gives the alarm. In order to make the right decision, we need to know: where is the source of the contamination ? Where is it coming from and where is it going to? Without this information we will not be able to initiate countermeasures.
Of course, the number of sensors has to be minimized. Firstly because of costs and secondly, maintenance and operating expenses

## Slide 7
SMaRT-OnlineWDN
Online Security Management and Reliability Toolkit
for Water Distribution Networks
main Objective:
To develop an early warning system and a decision support toolkit for emergencies and the deliberate contamination of WDN
Notes: AND this was exactly What motivated us to come up with Smart online
So … what does Smart online stand for:… And our main objective is to devel……..

## Slide 8
German Partners
Enduser and Coordinator:
Berlin Water
Industry Partner:
3S-Consult
Research Partner:
DVGW-Technology Center for
Water
Fraunhofer Institut für Optronik,
Systemtechnik und Bildauswertung
(IOSB)
French Partners
Endusers:
Communauté urbaine de Strasbourg
Veolia Eau d‘IIe de France
Industry Partner:
Veolia Environment Recherche & Innovation
Research Partners and Coordinator
Engees: École nationale du Génie de l‘eau et de l‘environnement de Strasbourg
Irstea: National Research Institute of Science and Technology for Environment and Agriculture
Consortium
Notes: this diverse consortium ( resarch partner, institute represent highly competent and expierenced organisations in this field.

## Slide 9
Decision Support Tool:
Notes: This picture demonstrates the decision support toolkit, which will be developed by SMaRt Online ;
It consists of three main parts; Monitoring; Simulation and decision making:
Imagine a sensor network as a combination of different sensor types has already been set up. E.g. toxicity, quality and hydraulic sensors. The sensor data is transmitted in real time to Utilities scada system; These will be evaluated by the alarmgeneration.
Once a contamination is identified, the online running model,which is automatically calibrated to the measured sensor data, simulates the current hydraulic status of the WDN by using offline and online data.
Next up, the source identification tool automatically switches on and locates the contamination source by using the look back modus and the transport model. The spread of contamination is then found out by simulating the future hydraulic status and using a forecast on water demand.
This not only allows us to have a look ahead but to evaluate decisions as well. For example, simulating some scenarios for flushing the pipes in contaminated area and see the results.

## Slide 10: Optimal Sensor Placement for all three cities
      Biggest water distribution network
      in France with 8 000 km pipelines
      200 water quality sensors in the WDN
VEDIF, Paris area
Main Results of the Project
Notes: In the following slides I only show the main Parts of the project and give you an idea
of the results we have achieved so far …
Three of my colleagues ( fellow researchers) will talk about the results, more detailed,
In Paris sensor placement is beeing tested by installing 200 qulity sensors..

## Slide 11: Alarm Generation Module
Training from historical data (method: Principal Component Analysis)
Software module with GUI developed
Oxygene
Conductivity
Redox
pH
Turbidity
Notes:   the alarm must be reliable

## Slide 12: Online Simulation on Real Networks
Strasbourg
Paris
Berlin
Notes:   Online simulation should Reflect the current hydraulic status and monitor the water quality
  In addition it should have an Automatic calibration

## Slide 13: Source Identification
water source
positive sensor alarm
negative sensor alarm
consideration of positive
and negative alarms
online monitoring of areas
observed by sensors (node-
time-pairs)
Notes: Topologigcal Graf based
Irstea: partical Back tracking by using the transport modell
Irstea: Adjoint methode: Solving invers Transport

## Slide 14
Experiments on real Pipe Network
abandoned
Representative of water pipes in Germany and Europe
Notes: the behaivior of contaminant like Adsorption should be investigated by experiments at a real world network

## Slide 15: A real Test Network at TZW Dresden
Notes:   It was shown that incomplete mixing occurs in some configurations
  CFD results were validated on experiments, and an imperfect mixing

## Slide 16: Transport Model at Junctions and Crossings
Double Te- Junction
Kriging interpolation result for the case distance = 5D and Reynolds = 1,000
complete mixing??
Notes:   Transport model should help Tracing substances
  Our objective was focusing on Junction and Crossings.
  Often it is simply assumed that substances are completely mixed

## Slide 17: Risk Analysis and social Impact Assessment
Real impacts and perceived ones are performed for the three aspects of sustainability: - environmental - social - economic, combined with technical innovation
Notes:   Evaluation of potential risks, impacts, their causes and possible consequences

## Slide 18
1: SMaRT-Online WDN Perspectives
water utilities need to find a cost effective way to provide models with real time information
2: Further research Work
Improving the resilience of network system…
How to move on…
Notes: This was an overview of our projekt; The following presentors will give more detailed information about different aspects of the project.
´before we continue I,m happy to answer any….

## Slide 19
Thank you for your attention
Any questions?
www.smart-onlinewdn.eu
Fereshte.Sedehizade@bwb.de

## Slide 20
5.4 m³/h
5.4 m³/h
Inject: 70 L/h
Conc. 280 g/L
out flow data
Reynolds number: 10,000
Injection | S1 | S3 | S2 | Velocity [m/s] | Distance | calc./measur. travel time [min] | max. concentration [g/l]
12:28 | 12:37 |  |  | 0.095 | 42 | 7.37 | 3.09
12:28 |  |  | 13:51 | 0.095 | 191 | 84.56 /83 | 3.00
12:28 |  | 13:00 |  | 0.095 | 482 | 33.51 /32 | 2.78
S1
S3
S2
2.78
3.09
3.00
Adsorption ~ 16%

## Slide 21: Main Results
1: Optimal sensor placement
  200 multi-probe sensors were set at optimal locations (VEDIF)
2: Alarm Generation
  A software solution was delivered for online alarm generation that is based on Principal Component Analysis.
3: Online Simulation model
  Enhanced hydraulic network simulation by means of graph simplification
  Source Identification
4: Transport Model
  A TZW pilot scale set that is designed according statistics of Tee, Cross and N-junctions on real networks.
  It was shown that incomplete mixing occurs in some configurations
  CFD results were validated on experiments, and an imperfect mixing module released (lookup table + interpolation)
SMaRT-OnlineWDN